# SC-SD-I夹缝式涂布机

# 名称：夹缝式涂布机；                                品牌：北京赛德凯斯；

厂家：北京赛德凯斯电子有限责任公司；                型号：SC-SD-I

公司产品链接网址：http://setcas.com/?page_id=4615

# 夹缝式涂布机

- SC-SD-I型夹缝涂布机技术参数如下：

| 名称 | 夹缝式涂布机 |
| --- | --- |
| 品牌 | SETCAS |
| 产地 | 美国 |
| Slot-Die Head Coating Width | 50 mm (maximum) |
| Slot-Die Shim Thickness | 100 μm |
| Hotplate Temperature | 120 °C (maximum) |
| Stage Travel Length | 100 mm (maximum) |
| Minimum Stage Speed | 100 μm.s-1 |
| Maximum Stage Speed | 50 mm s-1 |
| Minimum Syringe Speed | 12 μm.s-1 |
| Maximum Syringe Speed | 5 mm.s-1 |
| Maximum Head to Substrate Travel Distance | 13 mm |
| Power Supply | DC 24 V, 6.2 A, via 100-240v 50/60Hz power adapter |
| Dimensions | Depth x Width x Height (360 mm x 280 mm x 190 mm) |
| Shipping Weight | < 10 kg |

# SC-SD-I Slot Die Coater

| Description | Slot Die Coater |
| --- | --- |
| Brand name | SETCAS |
| Origin | USA |
| Slot-Die Head Coating Width | 50 mm (maximum) |
| Slot-Die Shim Thickness | 100 μm |
| Hotplate Temperature | 120 °C (maximum) |
| Stage Travel Length | 100 mm (maximum) |
| Minimum Stage Speed | 100 μm.s-1 |
| Maximum Stage Speed | 50 mm s-1 |
| Minimum Syringe Speed | 12 μm.s-1 |
| Maximum Syringe Speed | 5 mm.s-1 |
| Maximum Head to Substrate Travel Distance | 13 mm |
| Power Supply | DC 24 V, 6.2 A, via 100-240v 50/60Hz power adapter |
| Dimensions | Depth x Width x Height (360 mm x 280 mm x 190 mm) |
| Shipping Weight | < 10 kg |